## Slide 1
A COMPARATIVE EVALUATION OF GREEN STORMWATER INFRASCTRUCTURE TOOLS:
CO-BENEFITS AND ALTERNATIVE FUNDING
By: Olivia Nichols, Master of Science in Applied Geosciences, Fall 2021
Primary Reader: Dr. Mazdak Arabi
Secondary Reader: Mitch Cron
Introduction
Methods
Results
Works Cited
Discussion
Table 1: Co-Benefit Results for the Green Values Tool
Conclusions
The Green Values Tool has the least amount of translations needed, the least amount of inherent assumptions, is the easiest to use, has the second highest number of co-benefit’s, shows the second highest number of alternative funding locations, offers a cost analysis, has the highest runoff percent change but a more sedate volume captured, and offers some water quality assessment.
The EPA Stormwater Tool has the most translations needed, the second most inherent assumptions, is moderately difficult to use, has no co-benefits, only helps with water based funding opportunities, offers a cost analysis, has the most consistent runoff percent change but no volume captured, and does not touch upon the change in water quality.
The CLASIC Tool has the second highest translations needed, the highest inherent assumptions, is moderately difficult to use, has the most co-benefits, has the most alternative funding locations, shows a cost analysis, shows the percent change in runoff and volume captured, and offers a comprehensive analysis of the change in water quality.
All three have their strengths and weaknesses, but knowing that these tools are available can help businesses, communities, and governments to identify alternative funding and encourage more GSI projects.
One inch of rain falling on one acre of land, the size of a football field, is equivalent to 27,154 gallons of water. And the North America average precipitation rate is up by 1.81 inches, so imagine an extra 50,000 gallons of water hitting the aging infrastructure and causing damage (Assessing the U.S. Climate in 2018, 2018). One way to reduce that pressure is to implement Green Stormwater Infrastructure (GSI), which directs runoff back into the earth via infiltration and reduces flows to sewer systems and surface waters. There are different co-benefits associated with each type of GSI, ranging from improvements in water quality, to money saved in energy bills, to even saving lives from heat related deaths (CNT, 2011). By focusing on comparative analysis of 3 different GSI tools, and what specific co-benefits they each offer details of, clearer recommendations on GSI projects can be made to multiple communities and may offer clarity on where to pursue additional funding for the implementation of GSI.
Assessing the U.S. climate in 2018. (2019-02-06T08:14:23-0500). Retrieved from http://www.ncei.noaa.gov/news/national-climate-201812
CNT. (2011). The value of green infrastructure: A guide to recognizing its economic, environmental and social benefits. Retrieved from https://www.cnt.org/publications/the-value-of-green-infrastructure-a-guide-to-recognizing-its-economic-environmental-and
Green Stormwater Infrastructure Tools
Green Values National Stormwater Management Calculator
Environmental Protection Agency’s National Stormwater Calculator
Community-enabled Lifecycle Analysis of Stormwater Infrastructure Costs tool (CLASIC)
Base Data
5 Rain Gardens (Projects 1-5)
15 Data Sets
Analysis Criteria
Degree of Translation
Inherent Assumptions
Co-Benefits
Costs (Initial Costs, Maintenance Costs, Lifecycle Costs)
Water Quality Change
Alternative Funding Potential
Direct Comparison (Runoff, Volume Captured)
Evaluation of Results
All Criteria will be compared
Ease of Use
Scale of Intended Use
Recommendations on Use and Combinations
Green Values | Project 1 |  | Project 2 |  | Project 3 |  | Project 4 |  | Project 5 | 
Co-Benefits | Annual | Lifecycle Benefits | Annual | Lifecycle Benefits | Annual | Lifecycle Benefits | Annual | Lifecycle Benefits | Annual | Lifecycle Benefits
Reduced Energy Use from Trees |  |  | $36.00 | $732.58 | $180.00 | $3,662.91 | $360.00 | $7,325.82 | $576.00 | $11,721.31
Community Total | $31.30 | $636.93 | $316.36 | $6,437.75 | $1,413.42 | $28,762.42 | $2,991.75 | $60,880.64 | $4,755.37 | $96,769.44
Reduced Air Pollution from Trees |  |  | $0.18 | $3.68 | $0.91 | $18.42 | $1.81 | $36.83 | $2.90 | $58.93
Carbon Dioxide Sequestration from Trees |  |  | $0.12 | $2.44 | $0.60 | $12.21 | $1.20 | $24.42 | $1.92 | $39.07
Compensatory Value of Trees |  |  | $275.00 | $5,596.11 | $1,375.00 | $27,980.55 | $2,750.00 | $55,961.09 | $4,400.00 | $89,537.75
Groundwater Replenishment | $23.25 | $473.05 | $30.49 | $620.53 | $27.42 | $557.95 | $177.31 | $3,608.23 | $260.36 | $5,298.16
Reduced Treatment Beneftis | $8.05 | $163.89 | $10.56 | $214.98 | $9.50 | $193.30 | $61.43 | $1,250.06 | $90.20 | $1,835.53
Total | $31.30 | $636.93 | $352.36 | $7,170.33 | $1,593.42 | $32,425.33 | $3,351.75 | $68,206.45 | $5,331.37 | $108,490.75
CLASIC | Project 1 | Project 2 | Project 3 | Project 4 | Project 5
Economic Co-Benefits |  |  |  |  | 
Property Values |  |  |  |  | 
Avoided Costs from Illness |  | 2.3 | 5 | 3.7 | 3.7
Avoided Costs from Combined Sewer Treatment |  |  |  |  | 
Potential impacts from Nuisance Floods |  |  |  |  | 
Building Energy Efficiency |  |  |  |  | 
Avoided Water Treatment |  |  |  |  | 
Employment Opportunity | 2.6 | 3.1 | 2.7 | 3.4 | 5
Social Co-Benefits |  |  |  |  | 
Health Impacts form Air Quality |  | 2.3 | 5 | 3.7 | 3.7
Mental Health | 2.3 | 2.3 | 5 | 3.5 | 3.5
Thermal Comfort |  |  |  |  | 
Increased Supply from Harvested Stormwater |  |  |  |  | 
Public Awareness of Stormwater and Water Systems | 3.3 | 3.6 | 4.1 | 3.1 | 3.7
Potential Avoided Social Strain Associated with Nuisance Flooding | 2.7 | 2.7 | 5 | 3.2 | 3.2
Environmental Co-Benefits |  |  |  |  | 
Ecosystem Services | 1 | 1 | 1.7 | 1 | 1
Groundwater Flow | 2.8 | 2.8 | 5 | 3.1 | 3.1
Carbon Sequestration |  |  |  |  | 
Table 2: Co-Benefit Results for the CLASIC Tool
Alternative funding possibilities and opportunities are found by analyzing the co-benefits suggested by each tool as those provide potential places or groups that might be interested in funding GSI projects. By investigating who exactly would benefit from a co-benefit of a GSI project, it becomes possible to identify and encourage multigroup funding.
The Green Values Tool shows 7 different co-benefits, all shown in Table 1. The Green Values Tool would recommend via this method to look for groups already supporting increasing property values, dealing with groundwater treatment, or helping with pollution.
The CLASIC Tool reports 8 co-benefits, as seen in Table 2. Alternative funding might be found in wellness groups, hospitals, local gardens, and anywhere that anyone has to deal with nuisance flooding. Using the GSI Tools co-benefit results as a first step in locating places where cases can be made for alternative funding is a great way to help more projects come to fruition.